#### URDF:
- Domain-specific modelling language (DSML)
- ROS specific file-format based on XML
  - Stores
- Robot body layout (kinematic structure)
- Appearance
- Extra information (joint limits, mass, etc)
Uses names and concepts from the robotics domains
#### URDF Implementation:
- Text file
- XML tags standardized in URDF standard
- File references using Uniform Resource Locators (URLs)
- 3D mesh files
#### Contents:
- Mostly <link> and <joint> elements
- <link>s: form the robot's structure
- <joint>s: form the connections between links and set motion constraints
#### Joint types:
- Fixed: rigid connection, no motion
- Revolute: support rotation in 1 dimension (along a single axis)
- Continuous: unlimited variant of revolute joints
- Prismatic: support translation in 1 dimension (along a single axis)
- Planar: translation in two dimensions
- Floating: unlimited motion (translation and rotation) in all 6 dimentions
#### Standardisation:
- REP 103 - Standard Units of Measure and Coordinate Conventions
- ROS uses a right-handed coordinate system : X+ (forward); Y+ (left) then Z+ (up)
- ROS uses SI units for everything:
- Length: meters
- Angles: radians
If we draw this robot we might see something like this:

This is obviously not a very useful robot, as it is very small and cannot do any useful work. But it is a valid URDF and shows the basic building blocks of any URDF: link and joint elements and their properties.
#### Limitations:
1. Robot description cannot be changed (immutability)
2. Only tree structures (no loops)
  3.No <sensor></sensor> (no sensor models)
  4.Low reusability of URDFs (composability)
#### Limitation 1 - Immutability:
- Result of typical control flow
- Robot description read once from  server
- No standardized way to notify
- Risk of desynchronization
#### Limitation 2 - No cycles:
- Joint only have single parent and child
- Only acyclic, directed graphs (or: trees)
- Real-world impact
#### Limitation 3 - No sensor element:
- Sensor meta-data can't be incorporated directly
- Alternatives exist, but then the data is distributed
- Diminishes value of URDF
#### Limitation 4 - Low reusability:
- Only a single <robot> tag in URDF
- No support for import of remote files
- Composite scenes have to be merged manually
- No way to compose multiple
The solution to some of these problems can be XACRO (short for XML Macros)
- Programmatic URDF generation
- Templates
- Parameters
#### XACRO and Composability
- Import macros from other files
- Parameterize templates
- Composite robots & scenes easier:
- import macro from file
- Invoke macro
#### XACRO - Needs conversion
- XACRO not directly compatible with URDF
- Transformation needed with this command:
  $ rosrun xacro xacro /path/to/robot.xacro > robot.urdf
- Checks for valid XACRO file (but is not identical to check_urdf)
  And as always, to convert the entire XACRO file to URDF, we use the following command:
  rosrun xacro xacro tiny_robot.xacro > tiny_robot.urdf
This will cause the lines between <xacro:macro> and </xacro:macro> in the macro definition above to be automatically inserted (ie: copy-pasted) into the URDF file that will be generated by the conversion process.
All of this makes XACRO a really powerful system: XACRO files can import other XACRO files, macros can call other macros and parameters can be used to add flexibility to macros.
#### Summary:
It is easy to make mistakes in URDFs, as they can become many hundreds if not thousands of lines long in real ROS applications.
Luckily ROS provides us with a tool that we can use to verify the correctness of our URDFs: check_urdf. We can run it like so:
  check_urdf robot.urdf
This tool only checks the syntax though, so it checks whether we've only used legal combinations of recognized URDF keywords in our files. It cannot check whether you've correctly specified the mass of your robot links, whether the model that we've created makes sense or whether the colors that you've used correspond to what the manufacturer has used.
One other thing that check_urdf cannot do directly is checking XACRO files.
We can however verify the URDF that they will generate, so we can first convert them and then run check_urdf on the resulting file.
So we first convert the XACRO file to URDF (this will generate the URDF file in the current working directory):
  rosrun xacro xacro /path/to/robot.xacro > robot.urdf
And then run check_urdf on that file:
  check_urdf robot.urdf
This will check our URDF, but we must then map any mistakes it finds back to our XACRO files ourselves.
To get the factory simulation ready the following tasks need to be done:
- Remove unneeded bins
- Move bin to turtlebot delivery station
- Add a pedestal
- Add the second robot
We suggest opening the URDF (.xacro file) using a text editor with support for XML highlighting, for example Atom, since it makes reading the file easier
A few notable parts of the URDF are:
- A link named "world": a link that everything else is connected to
- There are also links created that instantiate other URDF models like the conveyor belt
- After importing all of the building blocks of the world, it is important to then connect them to the world using joints
- The "parent link='..'" specifies to what something should be connected and the "child link='..'" specifies what it is that should be connected to the parent.
- the origin element describes the relative offset between the parent and the child
To remove a model from a URDF world two things must be removed:
- The joint that connects it to its parent
- The "macro call" that adds it to the world (model instantiations)
To remove four bins, the four model instantiations (ie: macro calls) and the four joints need to be removed.
We leave one bin and relocate it to where it should be (behind the pallet with the crates) by changing the x and y coordinates of its origin element.
A useful tool is "check_urdf", which can check if a URDF is valid. To do this, first convert the XACRO file to URDF, and then run check_urdf.
We can use primitive shapes to model complex geometry in a simple way.
We will use such a primitive shape to create a box we can place our second robot on. Open your hrwros.xacro file in a text editor. Scroll all the way down to the bottom. We will need to add two things: a link, and a joint. You will need to give it a name, and this name is important! It must be unique, and should make the purpose of the link clear.
Before it will become visible in the simulation, we will need to give it a visual element.
With the link and joint in place, we can take a look at what we've created. First, save the URDF, then switch to the terminal, and start the visualization launch file.
We've added the box, but we still need to modify it a little more before it becomes usable. We have defined the basic structure, and have connected it to the world. We will still need to update the dimensions, specify a color, place it on the floor, and put it next to the bin.
- The current status of the pedestal is not yet satisfactory to the factory simulation. To make a proper pedestal, some default properties of the primitive shape need to be changed:
- Adjust the size and shape
- Raise the pedestal so that it rests on the floor
- Change the color
- Update its location
The box can be made taller by updating the "size" property (following the x, y, z convention of ROS to configure the width, length and height respectively).
The default origin for primitive shapes is the center of the shape, which means that the box is half sunk into the floor. To fix this, the z offset of the origin needs to be changed to half the height of the pedestal.
Colors are added by adding a "material" element. Since the pedestal is one solid color the "color" element is used to specify the color with rgba.
To change the location of the pedestal, the offset from the world needs to be redefined. This is done by changing the x and y coordinates of the "origin" element within the joint that connects the pedestal to the world (note: not the definition of the origin in the primitive shape itself).
To finish up the factory floor the second robot needs to be added to the world. Instead of using simple geometry to create our own robot, we will import a detailed model that was made by the ROS community. This is one of the advantages of ROS, allowing us to save time and work by using pre-existing models instead of having to create them ourselves.
In order to add the robot to the factory, the following changes need to be made to the hrwros.xacro file:
- Import the model definition (xacro macro)
- Add the model to the factory (instantiation)
- Fixing it in place (joint)
- Updating orientation
The import statement consists of a few parts:
- The xacro:include statement itself
- The filename attribute specifying the name of the file to import (using a package relative path)
Finally, we also need to add the macro call, which will actually instantiate the model. To prevent nameclashes, we'll configure the new object to use a unique prefix (using the "prefix" parameter of the macro).
To connect the robot to the factory, we will connect it to the pedestal rather than the world itself. This is so that if the pedestal ever needs to be moved, the robot will move with it, rather than having to update the robot's position manually. This is done by specifying the parent in the joint as the pedestal and the child as the robot.
Finally, the orientation needs to be corrected. This is done by adding an rpy attribute to the origin element that specifies the orientation. As ROS uses radians for angles, we'll make use of the radians(..) convenience function which will do the conversion for us.